|  | ......................... Pc. .............................. € .............................. € GEZE F 1200+ System Drive system for inward opening turn-and-tilt / bottom-hung windows for daily ventilation and exhaust. Drive system consisting of a drive unit, the F 1200+ and the F 1200 turn-and-tilt hardware. Automated tilted position to opening width of 180 mm without chain and manual opening in turning position. In disconnected mode, mechanical emergency locking and unlocking is possible. Drive with integrated operating element and handle function for motorisation of the associated hardware. The number of horizontal/vertical central locking systems depends on the closing force of the leaf. Application Leaf dimensions: ........ mm width (min. 750 mm – max. 2400 mm) ........ mm height (with vertical operation by F 1200+ min.980 mm – max. 3500 mm) (with horizontal operation by F 1200+ 750 mm – max. 3500 mm) Opening width with tilt opening: 180 mm Leaf weight: max. 200 kg (corresponding application diagram can be found in the installation drawing |
| --- | --- |
|  | ......................... Pc. .............................. € .............................. € GEZE F 1200 turn-and-tilt hardware Turn-and-tilt hardware Cranked turn-and-tilt hardware for convenient and simple operation of large and heavy aluminium windows. The hardware consists of a surface-mounted hinge side and a concealed central locking mechanism. Hardware properties Usable in aluminium profile systems Schüco, Hueck, Wicona with the following hardware chamber dimensions: Leaf groove: 21 mm Frame groove: 14 mm Groove depth push rod: 6.5 mm Rebate space: 16 mm Hardware design Colour hinge side: ( ) EV1 / ( ) according to RAL Type of installation / installation position: ( ) DIN R / ( ) DIN L |
|  | ......................... Pc. .............................. € .............................. € GEZE F 1200+ drive Ventilation drive for automation of inward opening turn-and-tilt and bottom-hung windows. Usable only with F 1200 hardware Functions: Electrical locking and unlocking of the hardware in real time with manual turn function plus motorised tilt ventilation for the ventilation mode of tilt and turn and bottom-hung windows with variable adjustment. The high quality aluminium drive unit serves as an ergonomic handle element with manual operation in the turning position. Use of the turning position can either be completely deactivated, or enabled for authorised persons only. Automatic mode enables extremely quiet-running operation. Operating unit with capacitive control keys with LED backlight enables intuitive operation with recommended actions and so prevents misuse by the user. An LED status display shows the opening indication, the operating mode as well as warnings in the event of misuse. Precise control of the operating field by means of proximity sensor to identify when the user is approaching or moving away, and brightness sensor to adjust the ambient brightness. In disconnected mode, the drive can be moved by means of mechanical emergency unlocking. Application Designed for the GEZE F 1200 tilt and turn hardware for leaf heights up to 3.5 m with a maximum leaf weight of up to 200 k (note special groove geometry and application diagrams for the hardware). Opening width with tilt opening: 180 mm Activation Manual operation via integrated operating field on the drive and integration in the building automation in conjunction with GEZE IQ box KNX possible. Installation The drive unit can be installed both vertically and horizontally. A cable transition from the frame to the leaf can be designed as divisible line transition. Pinch protection Up to protection class 3 according to the Machinery Directive EC/42/2006 without additional sensors thanks to reduced closing speed. In conjunction with the GEZE IQ box Safety and suitable sensors, protection class 4 is possible (according to safety analysis). Technical data Supply voltage: 24 V DC / ± 10 % Current consumption: max. 2.5 A Duty rating: ED 30 % Power consumption: 60 W Ambient temperature: -5 °C to +70 °C Unlocking time: < 4s Sound pressure level: < 38 dbA (automatic mode) Speed (tilt) automatic operation 11 mm/s on main closing edge Speed (tilt) manual up to 32 mm/s on main closing edge Housing IP rating: IP40 Housing: aluminium Dimensions: 506 x 53 x 45 mm (W x H x D) Installation position: ( ) vertical / ( ) horizontal Surface: anodised EV1 Colour: ( ) EV1 / ( ) according to RAL.......... Side cap: ( ) RAL 7012 / ( ) according to RAL.......... Version Type of installation / installation position: ( ) DIN R / ( ) DIN L Turn function: ( ) enabled ( ) mechanical turn block (key) ( ) software-controlled turn block |
|  | ......................... Pc. .............................. € .............................. € Cable transition Concealed cable transition in the rebate space for power supply of the window drives. Cable transition with detachable connection. Application To provide power supply to drives that are mounted on the window leaf Leaf and frame installation Version ( ) Cable transition 4 m / 6 m ( ) Cable transition 2 m / 3 m |
|  | ......................... Pc. .............................. € .............................. € Power supply – NT 6.25 A – 24 V HS power supply Power supply for top hat rail mounting and to supply 24 V drives and control units. Technical data Output voltage: 24 V DC Operating voltage: 230 V +/- 10% Output current: max. 6.25 A IP rating: IP20 Version Top hat rail housing: grey Size W x H x D [mm]: 72 x 95 x 66.5 Material: plastic |
|  | ......................... Pc. .............................. € .............................. € Surface-mounted housing Housing for surface-mounted installation of top hat rail components such as power supplies or control units. With integrated 35 mm top hat rail for devices with a max. of 7 division units (18 mm). Technical data IP rating: IP 40 Cable routing surface-mounted or flush-mounted Version Size W x H x D [mm]: approx. 193 x 130 x 82 Colour: white Suitable for cascading Material: plastic |
|  | ......................... Pc. .............................. € .............................. € IQ box KNX For connection of the window drives of the GEZE IQ windowdrive series to the KNX building system for intelligent natural ventilation. The IQ box KNX is compatible with the following GEZE window drives from software version 3.0: E 250 NT spindle drive Slimchain chain drive Powerchain chain drive Power lock locking drive F 1200+ Activation of the connected drives (position in %, speed in %) as well as feedback on the current position and window status (closed / open / opening /closing / position) is implemented by the KNX building bus. Ventilation functions gap ventilation and timed ventilation must be guaranteed without further controls. Technical data Supply voltage 24 V DC,+-25 %, SELV Max. current drives 6 A Induced current intake to KNX-bus 5 mA Induced current intake to 24 V 25 mA IP rating / protection class IP 20 protection class III Ambient temperature 5 °C .. +70 °C Connection cross-section 24 V & drive 1.5 mm² Connection cross-section push button 0.5 mm² Max. overall length of drive cable 15 m Dimensions of flush-mounted housing (UP) 50 mm x 45 mm x 19 mm Dimensions of top hat rail housing (HS) 98 mm x 62 mm x 18 mm (2 DU) Housing version ( ) Flush-mounted housing IQ Box KNX UP ( ) Top hat rail housing IQ-Box KNX HS |
|  | ......................... Pc. .............................. € .............................. € IQ box Safety HS TÜV-tested safety switching device for protection of the main and secondary closing edges of power-operated windows, hatches and skylights etc. in combination with safety edges and/or non-contact sensors. TÜV-certification in accordance with the Machinery Directive 2006/42/EC. One IQ box Safety is needed per window. If danger is detected by the sensors, the power-operated window stops or reverses the movement and prevents the risk of injury. Properties Fulfils the highest protection class specifications for power-operated windows according to the risk assessment performed in accordance with Machinery Directive 2006/42/EC (protection class 4) For natural ventilation (24V power supply, KNX, IQ gear) and/or smoke and heat extraction systems (SHEV control unit) DIP switch for (de)activating the sensor inputs. Adjustment to the parameters with ST 220 service terminal possible Top hat rail housing with plug-in terminals for easy wiring Integrated push button for closing windows manually during servicing Connection possibilities IQ box Safety is compatible with the GEZE IQ windowdrive window drives (24 V DC) from software version V3.2: E 250 NT spindle drive (also in smoke and heat extraction opening and locking systems) Slimchain chain drive Powerchain chain drive Power lock locking drive F1200+ from software version 1.0 Pre-set inputs for non-contact sensors, e.g. GC 339 or GC 342 Pre-set inputs for safety edges (terminating resistor from 4.5 k to 22 kOhm) Technical data Supply voltage 24 V DC, +-25 % Max. current drives 10 A Ambient temperature -5 °C…+70 °C Max. connection cross-section 2.5 mm² Max. length of the line to the drive 50 m Max. sensor line length see technical data of the respective sensor Dimensions of top hat rail casing (HxDxW) 90 mm x 60 mm x 35 mm (2 division units) Certifications TÜV, EN ISO 13849-1:2016-06 and DIN EN ISO 134849-2:2013-02; Safety of machinery - Safety-related parts of control systems Note In accordance with Machinery Directive 2006/42/EC a risk assessment must be prepared for power-operated windows. The GEZE safety analysis for power-operated windows can serve as a guide for the risk analysis. These specifications determine the necessary protection class of the window and the definition of the protective measures. As the types of window and installation and the structural features of the buildings vary greatly, it is always advisable to undertake a feasibility study beforehand (especially in the case of retrofitting). |
|  | ......................... Pc. .............................. € .............................. € Sensors for protection (optional position) Safety edges and/or non-contact sensors for protection of the main and secondary closing edges on the window Definition of the window to be protected ( ) Inward opening ( ) Turn-and-tilt window ( ) Bottom-hung window ( ) Side-hung window other types of leaf available on request …………mm width …………mm height …………mm installation height …………mm opening width |
|  | ......................... Pc. .............................. € .............................. € GEZE GC 342 laser scanner (optional position) Self-monitored laser scanner to protect the main and secondary closing edges of the window. Technical data IP rating IP54 max. detection area 4 m (diagonal) Min. installation height 2500 mm Max. installation height 3870 mm Version ( ) outside ( ) inside ( ) stainless steel colour ( ) black ( ) white Protective cover to protect the laser scanner against interferences ( ) stainless steel colour ( ) black ( ) acc. to RAL and/or |
|  | ......................... Pc. .............................. € .............................. € GEZE GC 339 active infrared light curtain (optional position) Self-monitored light curtain to protect the main and secondary closing edges of the window. Technical data IP rating IP54 Detection area (for installation height 2.2 m) up to 2.2 x 0.35 m (W x D) 10 adjustable light curtain configurations Min. installation height 2000 mm Max. installation height 3000 mm Version ( ) outside ( ) inside Version ( ) stainless steel colour ( ) black ( ) white and/or |
|  | ......................... Pc. .............................. € .............................. € Safety edges (optional position) Safety edges to protect the main and secondary closing edges of the window. Terminating resistor between 4.5 k and 22 k Ohms for use with IQ box Safety. Dimensions of the window ….. Number of safety edges per window ….. Length(s) of the safety edge(s) ….. |
|  | ......................... Pc. .............................. € .............................. € Delivery and installation Delivery, installation and commissioning by plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection book. |