|  | ......................... pcs. .............................. € .............................. € MSW with IGG elements Manual sliding wall system GEZE MSW with integrated all-glass system IGG, made up of glass elements which are manually movable independently of each other, an aluminium track system, and a station to stack the elements which is dimensioned according to the number of elements in the system. Dimensions of the manual sliding wall Clear width: ............... mm Clear height: ….. mm (finished floor level to lower edge of ceiling max. 4000 mm) Number of elements: …. pcs. SmartGuide Enables the guiding side of the roller carriage in the track to be switched over without the use of external control or power feed. This means that even complex track curvatures can be realised while maintaining permanent guiding of the carriages. System layouts without swing door end panels allow the complete opening of the front of the system. Track system Smooth operation due to guided curve technology for easy operation of the elements, no sharp-angled or unguided branches. Carriage with permanently engaged guide rollers and mechanically coded track, either fixed or with auto-reversible guiding side, which makes it very simple to use and prevents maloperation. Carrier rollers fitted with quiet-running plastic rollers and sealed ball bearings, spherical discs or gliding discs are not permitted. Track made of extruded aluminium profiles with a cross-section of 96 x 66 mm. Ceiling end brackets installed on site are attached to the track by sliding blocks which can be supplied as an option. The track must be fixed to on-site load-bearing components (e.g. steel structures or similar). Track layout ( ) straight ( ) segmented (designed as mitre-cut up to 10°, above 10° using track bends) ( ) continuously curved Stacking area ( ) Position outside the frontage, without swing door end panels, using SmartGuide technology ( ) Positioned sideways in the system frontage using swing door end panels ( ) 90° stacking area (leaf elements at 90° to the system's direction of operation) ( ) Parallel stacking area (leaf elements parallel to the system's direction of operation) ( ) custom-designed stacking area according to drawing ( ) with double track (recommended for visible stacking areas) ( ) with single track (recommended for invisible stacking areas) Locking and floor guide ( ) Locking is in double eccentric floor sockets with interchangeable insert for optimal adjustment and fit. The elements are locked using hold-open mechanisms at their ends which lock into floor sockets that are supplied. To prevent the unauthorised levering, the elements are connected to one another by means of interlocking profile pins. Alternatively, a version featuring arresting front-mounted floor locks and integrated cover locks with a profile cylinder can be used to lock the elements. ( ) with floor guide Elements Leaf elements up to 1500 mm wide and 3500 mm high, weighing up to 150 kg. Upper and lower frame profiles feature integrated guide channels for securing the carriages, as well as locks and sealing components without additional add-on and connection profiles. Carriages' adjustment range +4/-7 mm for subsequent height compensation, e.g. if ceiling is sagged. The elements are made of an intrinsically stable, double-glazed permanently connected insulating glass construction with an interior concealed frame in the space between the panes of max. 27 mm for integration of the functional elements. The panes used must undergo a heat-soak test. There is a special hard-wearing coating on the backside of the edging of the panes (horizontal 50 mm, vertical 30 mm). Leaf joints are sealed by 2 silicone seals each of which is inserted into the facing profile. Sealed at the bottom and top with 2 integrated brush seals. Colour of surrounding edge printing RAL ..... Glass ( ) Clear glass quality (low iron oxide content, no green tinge) ( ) IGG comprising 2 x ESG-H 6 mm, 27 mm pane spacing (max. recommended height 3000 mm) ( ) IGG comprising 2 x ESG-H 12 mm, 27 mm pane spacing Subdivision of elements of the glass partitioning wall Locking by means of end-face locks or locks which can be operated from the inside, depending on the installation position. Initial locking on the stacking area side using a bolt lock for the profile cylinder which is installed on site. …. pcs. sliding panels …. pcs. swing leaves ( ) Single-action door with TS 3000 V ( ) Static swing door (no locking device) ( ) Static double-action door with floor spring TS 550 NV ( ) with door handle set ( ) with pull handle on both sides …. pcs. fixed panels |
| --- | --- |