|  | ......................... pcs. .............................. € .............................. € External flashlight for visual alarm indication Sturdy, maintenance-free and fail-safe design, xenon tubes for high visibility performance, one flash is emitted per second. For optional combination with external signal horn, flush-mounted, Polycarbonate housing; Operating voltage 20-30 V DC; Current consumption 90 mA; Protection rating IP 54 Dimensions (diameter x height): 93 x 72 mm Reflector colour: red |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € External signal horn for acoustic alarm indication With 26-fold adjustment signal tone, volume control from 74 - 94 dB (A) at distance of 1 m away with 24 V. Operating voltage 10-28 V DC, Current consumption 16 mA Protection rating IP54 Dimensions Surface-mounted:(diameter x height) 111 x 25.5 mm, Flush-mounted: 81 x 81 x 62.5 mm ( ) Surface mounting, white ( ) Flush-mounted installation, switch programme Jung AS 500 alpine white 62.5 mm deep flush-mounted boxes are needed for flush-mounted installation. |
|  | ......................... pcs. .............................. € .............................. € SLE 220 external fault indicator lamp for visual state or alarm indication Operating voltage 24 V DC; Current consumption 18 mA; IP rating IP 20 Surface mounting dimensions (W x H x D) 61 x 61 x 74 mm ( ) Reflector colour: red Flush mounting dimensions (W x H x D) 81 x 81 x 41 mm ( ) Jung AS 500 alpine white, reflector colour: green ( ) Jung AS 500 alpine white, reflector colour: red |
|  | ......................... pcs. .............................. € .............................. € SCT 320 external key switch Flush-mounted unit suitable for switch programme with dimensions of 55 x 55 mm. Including flat ribbon cable for connection to a GEZE TZ 32x door control unit Key switch with 2 microswitches for switching the functions short-time release, permanent unlocking, locking and for alarm reset Sabotage-proof cover With Euro profile half cylinder Colour: ( ) anthracite ( ) pure white ( ) alpine white Without frame |
|  | ......................... pcs. .............................. € .............................. € SCT 222 external key switch for authorised door passage, Connection to GEZE door control units, Bi-colour LED green/red for indication of the state unlocked/locked, yellow LED for indication of the alarm state Key switch with two-sided switching operation for Unlocking and short-time release/locking Complete with Euro profile cylinder and 3 keys IP rating IP 54 Dimensions (W x H x D): Flush-mounted: Front plate 100x110 mm; flush-mounted box 80x70x45 mm Surface-mounted: 80x70x45 mm ( ) Surface-mounted installation ( ) Flush-mounted installation RP 220 relay board or KL 220 clamping box necessary! |
|  | ......................... pcs. .............................. € .............................. € SCT 221 external key switch For authorised door passage by activating the short-term release function by key for installation on the outside or inside of the door, flush mounting or surface mounting possible without Euro profile half cylinder IP rating: IP 54 Dimensions (W x H x D) Surface-mounted: 75 x 75 x 50 mm Flush-mounted: 75 x 75x 61 mm, 50 mm deep flush-mounted box made of Zamak is included in the scope of supply. ( ) Surface-mounted installation ( ) Flush-mounted installation |
|  | ......................... pcs. .............................. € .............................. € SCT 220 UP external key switch for authorised door passage by activating the short-term release function by key, for installation on the outside or inside of the door, flush-mounted installation Complete with Euro profile cylinder in the single frame IP rating: IP 20 Dimensions (W x H x D): 81 x 81 x 62.5 mm Flush-mounted boxes 62.5 mm deep are needed for flush-mounted installation ( ) Jung LS 990 stainless steel ( ) Jung LS 990 alpine white ( ) Gira E2 pure white |
|  | ......................... pcs. .............................. € .............................. € FWS 320 B emergency exit sign Illuminated emergency push-button information label, flush-mounted Flush-mounted unit suitable for 55 x 55 mm switch programme. Integrated illuminated emergency push button information label with LEDs aligned in the same way Operating voltage 24 V DC Current consumption 30 mA Without frame ( ) Design in accordance with EltVTR |
|  | ......................... pcs. .............................. € .............................. € FWS 320 emergency exit sign Emergency push button information label, not illuminated, flush-mounted Suitable for 55 x 55 mm switch programme. Integrated emergency push button information label, not illuminated Without frame ( ) Design in accordance with EltVTR |
|  | ......................... pcs. .............................. € .............................. € Mounting for emergency push button information label Plexiglass with spacers Dimensions (W x H x D): 100 x 100 x 21 mm |
|  | ......................... pcs. .............................. € .............................. € PowerReserve STEP-UPS uninterrupted power supply To maintain the power supply to components of the GEZE escape route protection system and other GEZE door systems in the event of a power failure Properties Compact, low-maintenance and operationally reliable current buffer for top hat rail mounting for use with 24 V DC power supply, Equipment Integrated and long-life lithium-ion battery module, battery module replaceable, Integrated cyclical battery monitoring function, Integrated LED status display, 2 voltage outputs, 3 outputs to communicate the battery mode, charging status and alarm status, Buffer time can be set via rotary switch, Remote function to activate/deactivate the buffer function, Plastic housing; Technical data Rated supply voltage 24 V DC; Input voltage range 22.5 V DC – 29.5 V DC; Rated output voltage 24 V DC; Output voltage range 23 V DC – 26.5 V DC; Current consumption max. 4.7 A; Current consumption (when charging) < 0.5 A; Rated output current (continuous) 3 A; Output current max. 4 A; Capacity 46 Wh; Efficiency 98%; Dimensions (W x H x T) 108 x 90 x 71 mm; Weight 0.5 kg; Ambient temperature (operational) 0 °C – 40 °C; IP rating IP20; |
|  | ......................... pcs. .............................. € .............................. € RP 220 relay board for universal use in connection with TZ 320, for the connection of access control systems, key switch, motor locks and much more. |
|  | ......................... pcs. .............................. € .............................. € Log book for the documentation of acceptance tests and servicing |
|  | ......................... pcs. .............................. € .............................. € Toplock CTS V number code lock, in metal housing, with metal keypad with protection against vandalism, for entering 1 to 6-digit codes, incl. separate evaluating unit, on separate mounting plate Potential-free relay output, impulse 1 s Operating voltage: 230V AC IP rating: IP65 IP rating of the evaluating unit: IP43 Dimensions of the evaluating unit: 188 x 110 x 40 mm (W x H x D) ( ) CTS V (80 x 80 x 15 mm W x H x D) ( ) CTS BV with lighting (60 x 126 x 23 mm W x H x D) |
|  | ......................... pcs. .............................. € .............................. € NET 320 power supply For installation in flush-mounted box Plastic housing, cast module Input voltage: 230 V AC, 50 Hz Output voltage: 24 V DC (+/- 5%) Output current: 750 mA, 18W Dimensions: 55.7 x 33 mm (Ø x D) |
|  | ......................... pcs. .............................. € .............................. € NT 19.2-24 power supply For wall installation in plastic housing Input voltage: 230V AC Output voltage: Power supply 24 V DC Output current: 800 mA, 19.2 W IP rating: IP 54 Dimensions: 100 x 32 x 32 mm (W x H x D) |
|  | ......................... pcs. .............................. € .............................. € POWER SUPPLY NT 1.5 A-24V HS Technical data: Input voltage: 230 V AC Power: 36 W Output voltage: 21.6 - 26.4 V DC ± 1%, adjustable Output current: 1.5 A Version: Top hat rail housing, 2 division units Dimensions W x H x D [mm]: 35 x 90 x 58 |
|  | ......................... pcs. .............................. € .............................. € POWER SUPPLY NT 2.5 A-24V HS Technical data: Input voltage: 230 V AC Power: 60 W Output voltage: 21.6 - 26.4 V DC ±1%, adjustable Output current: 2.5 A Version: Top hat rail housing, 3 division units Dimensions W x H x D [mm]: 52 x 90 x 58 |
|  | ......................... pcs. .............................. € .............................. € Power supply NT 6.25 A-24 V HS Technical data: Input voltage: 230 V AC +/-10 % Power: 150 W Output voltage: 24 V DC +-3% (SELV) Output current: 6.25 A Version: Top hat rail housing, 4 division units Dimensions (W x H x D): 72 x 95 x 66.5 mm |